## Slide 1
IEEE RO-MAN 2026 · ORAL PRESENTATION
Ontology-Grounded LLM Planning
for Robust Table-Clearing Robot Manipulation
Planning over a grounded world model instead of free text
Satuk Buğrahan ÖZTÜRK¹ · Ahmet COŞKUNÇAY¹ · Erhan ÖZTOP²ʼ³ · Barış ÖZYER¹
¹ Department of Computer Engineering, Atatürk University, Erzurum, Türkiye
² Department of Artificial Intelligence, Özyeğin University, İstanbul, Türkiye ³ OTRI/SISReC, The University of Osaka, Japan
Notes: [ 0:00 - 0:40 ] TITLE Good morning. My name is Satuk Bugrahan Ozturk, from Ataturk University. This is joint work with Ozyegin University and the University of Osaka. Today I will talk about task planning for a robot that clears a table. Our claim is short. When a language model planner is tied to a symbolic world model, and that model is updated during execution, both plan quality and failure recovery improve substantially. Let me start with why that is harder than it sounds. (Adjust the name to whoever presents.)

## Slide 2
Ontology-Grounded LLM Planning · IEEE RO-MAN 2026
1
MOTIVATION
A simple instruction, a hard execution
“clear the table”
Natural language is a practical interface for human–robot interaction: the user states the goal, not the steps.
But the same sentence maps to a different action sequence in every physical scene.
1
Which objects are actually on the table right now?
Object set changes between and during trials.
2
Is any object blocked or stacked on another?
Support relations decide what can be picked first.
3
Does the scene still match the instruction?
The world moves while the plan is being executed.
A plan that is plausible at the text level can still fail in the actual environment.
Notes: [ 0:40 - 1:35 ] MOTIVATION Robots that work in shared spaces need a language interface. A user should be able to say: clear the table. And the robot should turn that into a sequence of meaningful actions. The hard part is not the sentence. It is everything the sentence does not say. The robot needs to know which objects are on the table right now. It needs to know what is stacked on what, because support relations decide what can be picked first. And it needs to know whether the scene still matches the instruction, because the world keeps moving while the plan is executed. So a plan that reads well as text can be infeasible the moment the arm starts moving. (Slow down here. Everything later depends on this gap.)

## Slide 3
Ontology-Grounded LLM Planning · IEEE RO-MAN 2026
2
PROBLEM
Why text-only LLM planning is brittle
1
Static scene description
The world state is written into the prompt once and then stays outside the execution loop. It is already stale by the second action.
2
No feasibility check
Nothing prevents the planner from proposing an action that conflicts with the physical preconditions of the scene.
3
No recovery path
One failed pick or one misplaced object invalidates the remainder of a long-horizon plan.
Prior grounding work helps — scene graphs, semantic maps and knowledge graphs give the planner explicit objects and relations [4]–[9] — but these representations are often only loosely connected to execution.
Notes: [ 1:35 - 2:25 ] PROBLEM Let me be concrete. Three things break a text-only planner. First, the scene description is static. The world state enters the prompt once, and then it sits outside the execution loop. By the second action it is already stale. Second, there is no feasibility check. Nothing prevents the model from proposing an action that violates the physical preconditions of the scene. Third, there is no recovery path. In manipulation, one failed pick invalidates everything after it. Scene graphs and knowledge graphs do improve grounding. But that representation usually stays only loosely connected to execution.

## Slide 4
Ontology-Grounded LLM Planning · IEEE RO-MAN 2026
3
RELATED WORK
Three lines of work — and the gap between them
LLM task planning
Instruction → symbolic action sequence
Long-horizon and service-robot planning
Corrective reasoning and feedback
[1]–[3], [10]–[15]
Vision–language grounding
Open-vocabulary 3D scene graphs
Scene-graph based task planning
Symbolic inputs derived from vision
[4]–[6], [19]–[26]
Knowledge-augmented planning
Object ontology knowledge for planning
Knowledge graphs for decomposition
Neuro-symbolic robotics
[7]–[9], [27]–[30]
The gap
A task state that persists through manipulation — queried again when a skill fails, not only when the first plan is generated.
Notes: [ 2:25 - 3:15 ] RELATED WORK Related work falls into three groups. The first uses language models as task planners, translating an instruction into a symbolic action sequence. The second improves grounding through perception, mostly with scene graphs as the intermediate representation. The third combines language models with explicit knowledge, such as ontologies and knowledge graphs. The closest work is Li and colleagues, who use object ontology knowledge for service-robot planning. Our difference is when the knowledge is used. We query the grounded state again every time a skill fails, so relations and target assignments are reused beyond the first planning request. (If you are behind schedule: skip the three groups, start from Li and colleagues.)

## Slide 5
Ontology-Grounded LLM Planning · IEEE RO-MAN 2026
4
CONTRIBUTION
What this paper contributes
1
Ontology-grounded state representation
Planning runs over a state built from ontology queries and simulator observations — never over free text alone.
2
Symbolic plan validation with bounded repair
Every plan is checked against permitted actions, known objects and the robot holding state before a single motor command is issued.
3
Failure-triggered replanning
When a skill reports failure, the state is reconstructed from ontology and simulator, and only the remaining task is replanned.
The contribution is the system-level integration of these three parts — evaluated end-to-end against a text-only baseline in PyBullet.
Notes: [ 3:15 - 4:00 ] CONTRIBUTION Our contribution has three parts. First, an ontology-grounded state. Planning runs over a state built from ontology queries and simulator observations, never over free text alone. Second, symbolic validation with bounded repair. Every plan is checked before a single motor command is issued. Third, failure-triggered replanning. When a skill fails, the state is reconstructed and only the remaining task is replanned. The contribution is the integration of the three. We evaluate the complete configuration against a text-only baseline.

## Slide 6
Ontology-Grounded LLM Planning · IEEE RO-MAN 2026
5
METHOD · SYSTEM OVERVIEW
Architecture: from instruction to grounded execution
Grounding sources
Natural language input
“clear the table”
Ontology world model
types · poses · support relations
Grounded state Sₜ
Sₜ = {Oₜ, Rₜ, Hₜ, Lₜ}
Symbolic planning
Simulator observations
current geometric configuration
LLM task planner
πₜ = F_LLM(x, Sₜ, 𝒜)
Plan validation
V(πₜ, Sₜ) ∈ {0, 1}
Execution and feedback
Validated symbolic plan
ordered pick / place sequence
Skill execution
predefined manipulation skills
Update or replan
Sₜ₊₁ = E(aₜᵏ, Sₜ)
Updated state after every action — and after every failure
Notes: [ 4:00 - 4:55 ] ARCHITECTURE This is the architecture. Please follow it from left to right. On the left are the grounding sources: the instruction, the ontology world model, and the simulator observations. These are merged into a single grounded state, S t. In the middle, the language model produces a symbolic plan from that state, and a validator accepts or rejects it. On the right, each validated action is mapped to a predefined manipulation skill and executed. The important part is the dashed line at the bottom. After every action, and especially after every failure, the state is rebuilt and fed back into planning. (Pause two seconds when the slide appears, before you speak.)

## Slide 7
Ontology-Grounded LLM Planning · IEEE RO-MAN 2026
6
METHOD · WORLD MODEL
Ontology as an actively maintained symbolic memory
Object types
Tableware · Cutlery · Containers · Food · Furniture
Pose properties
hasPosition (x, y, z) · hasOrientation (quaternion)
Support relations
onTopOf — is it on the table, stacked, or blocked?
Storage targets
Each semantic category maps to a default destination
EXAMPLE ASSERTIONS
plate1 rdf:type Tableware
fork1 rdf:type Cutlery
apple rdf:type Food
plate1 hasPosition [xp, yp, zp]
plate1 hasOrientation [qx, qy, qz, qw]
apple onTopOf fruit_bowl
After each action the manipulated object's pose and support relations are rewritten — the ontology is part of the execution loop, not a static description of the initial scene.
Notes: [ 4:55 - 5:45 ] ONTOLOGY WORLD MODEL Let me start with the world model. The ontology stores object categories, poses, spatial relations, and target assignments. The simulator gives us geometry. The ontology gives us the semantics we need to interpret that geometry in relation to the task. Support relations are expressed with onTopOf assertions. That is what separates removable tableware, supporting surfaces, and objects that are temporarily blocked. Each category is linked to a default storage target, so the planner does not treat all objects the same way. And it is not read-only. After every action, pose and support relations are rewritten. This ontology was defined manually for this domain.

## Slide 8
Ontology-Grounded LLM Planning · IEEE RO-MAN 2026
7
METHOD · GROUNDED STATE
Planning over a state, not over a paragraph
Sₜ = { Oₜ , Rₜ , Hₜ , Lₜ }
oᵢ = { cᵢ , pᵢ , qᵢ , ℓᵢ , sᵢ , bᵢ }
per-object symbolic record
Oₜ
Task-relevant objects
Table-related items only — furniture and unrelated entities are excluded.
Rₜ
Symbolic relations
Object-to-object and object-to-surface dependencies that gate manipulation.
Hₜ
Robot holding state
Flags an active grasp, so pick / place order stays consistent.
Lₜ
Available targets
Ontology-derived storage destinations for each category.
The complete ontology is never sent to the LLM. Only task-relevant knowledge is retained, which keeps the prompt small and prevents the planner from proposing actions that conflict with the physical scene.
Notes: [ 5:45 - 6:35 ] GROUNDED STATE Now the state itself. At any time step it has four elements. O t are the task-relevant objects. R t are the symbolic relations among them. H t says whether the robot is holding something. L t lists the available targets. For every object we keep a record: category, position, orientation, symbolic location, support relation, and a boolean for whether something blocks it. One practical point. We never send the complete ontology to the model. A larger ontology would need task-conditioned queries, so that only relevant knowledge enters the prompt.

## Slide 9
Ontology-Grounded LLM Planning · IEEE RO-MAN 2026
8
METHOD · PLANNING AND VALIDATION
Symbolic planning with a hard validity gate
PLANNING FUNCTION
πₜ = F_LLM ( x , Sₜ , 𝒜 )
𝒜 = { pick , place , move_home } — the planner stays purely symbolic; the prompt carries the instruction, the scene, the permitted actions and a required JSON schema.
VALIDATION FUNCTION
V ( πₜ , Sₜ ) ∈ { 0 , 1 }
Invalid plans are returned to the LLM together with the validation errors, for at most two repair attempts.
Non-empty plan
and only permitted actions from 𝒜
Known objects and targets
every referent must exist in Sₜ
Holding-state consistency
no pick while already holding an object
Correct place semantics
no place with an empty hand or the wrong object
Every validated symbolic action is mapped to a predefined manipulation skill — high-level reasoning stays decoupled from low-level control.
Notes: [ 6:35 - 7:25 ] PLANNING AND VALIDATION The planner receives the instruction, the grounded state, and the permitted actions: pick, place, and move home. It returns JSON. In the grounded configuration it returns ordered object-target pairs, which we expand into pick and place actions. Before anything executes, the plan is validated. We check that it is not empty and uses permitted actions only, that every object and target is known, and that the holding state is respected: no pick while already holding, no place with an empty hand. Invalid plans go back to the model with the errors, at most twice.

## Slide 10
Ontology-Grounded LLM Planning · IEEE RO-MAN 2026
9
METHOD · CLOSED LOOP
Failure is a trigger, not a dead end
1
Generate plan
2
Validate plan
3
Execute action
4
Observe outcome
5
Update world state
ON SKILL FAILURE
Reconstruct Sₜ from the latest ontology and simulator information
Replan only the remaining task, from the updated state
No separate external cue is given to the LLM
pick fails when
the object is unavailable, the robot already holds another object, an onTopOf relation blocks it, or grasp verification fails
place fails when
the hand is empty, the wrong object is held, the target is unknown, or the placement check fails
Ontology–simulator differences are recorded, but they do not independently trigger replanning.
Notes: [ 7:25 - 8:15 ] CLOSED-LOOP EXECUTION Execution is closed-loop. After each action we evaluate the outcome and update the world model. Every skill returns a success flag and an error description. A pick fails if the object is unavailable, if the robot already holds something, if an onTopOf relation blocks it, or if grasp verification fails. A place fails on an empty hand, the wrong object, an unknown target, or a failed placement check. On failure we reconstruct the state and replan only the remaining task. One point to note: no extra prompt tells the model that something went wrong. It finds out through state reconstruction.

## Slide 11
Ontology-Grounded LLM Planning · IEEE RO-MAN 2026
10
EVALUATION · SETUP
Table clearing in PyBullet with a Kuka LBR iiwa
Simulator
PyBullet — dining table, storage area, household objects
Robot
Kuka LBR iiwa manipulator
LLM backend
Qwen2.5 3B, served locally with Ollama
Decoding
4096-token context · 2048-token output
Objects
plate · cup · fork · apple container
Action space
pick · place · move_home
Two scenario families
Direct instruction following — “clear the table”, no disturbance
Execution-time disturbances — object moved, grasp failure, blocked object
120
trials in total
12 scenario definitions
× 5 repetitions
× 2 methods
Notes: [ 8:15 - 9:05 ] EXPERIMENTAL SETUP Now the evaluation. We use a Kuka LBR iiwa arm in PyBullet, with a dining table, a storage area, and four objects: a plate, a cup, a fork, and an apple container. The model is Qwen two point five, three billion parameters, served locally through Ollama. That small model is a deliberate choice. The weaker the planner, the more the world representation has to carry, so the effect of grounding is easier to see. Twelve scenarios, five repetitions, two methods: one hundred and twenty trials. The instruction was fixed throughout.

## Slide 12
Ontology-Grounded LLM Planning · IEEE RO-MAN 2026
11
EVALUATION · DESIGN
What is compared, and how it is measured
LLM-only planning (baseline)
Receives a simplified textual summary of the simulator state and generates the complete symbolic action sequence.
Ontology-grounded planning (proposed)
Receives table-related objects with their ontology-derived storage targets and returns an ordered sequence of grounded object–target transfers.
Same LLM backend · same validator · same robot skills · same replanning mechanism
Feasibility
Trials whose initial symbolic plan is valid under the current scene constraints
N_f / N × 100
Success
Trials in which the robot reaches the intended final task state
N_s / N × 100
Replanning
Disturbed trials in which the system recovers and completes the task
N_r / N_d × 100
Planning time
Mean time to generate a valid symbolic plan across all evaluated trials
(1/N) Σ Tᵢ
Notes: [ 9:05 - 9:35 ] WHAT IS COMPARED We compare two configurations. The baseline receives a simplified textual summary and generates the complete action sequence. The proposed method receives table-related objects with their ontology-derived targets. Everything else is shared: the same model, validator, skills, and replanning mechanism. We measure feasibility, task success, recovery on disturbed trials, and planning time. (Fast slide. Do not read the formulas.)

## Slide 13
Ontology-Grounded LLM Planning · IEEE RO-MAN 2026
12
RESULTS
Grounding improves feasibility, success and recovery
Chart: 
| Feasibility | Success | Replanning
LLM-only (text) | 8 | 12 | 17
Ontology-grounded | 44 | 64 | 73.3
INITIAL PLANNING TIME
65.5 → 15.2 s
≈ 77% faster to a valid plan
Feasibility
8.0% → 44.0%
Task success
12.0% → 64.0%
Replanning success
17.0% → 73.3%
Aggregate over the evaluated trial set (Table III). Planning-time gain should be read at the pipeline level: the two configurations use different output formats.
Notes: [ 9:35 - 10:30 ] AGGREGATE RESULTS These are the aggregate results. Feasibility of the initial plan goes from eight percent to forty-four percent. Task success goes from twelve to sixty-four percent. And recovery on disturbed trials goes from seventeen to seventy-three percent. That is the largest gap, and it is the one the design aims at. Planning time drops from sixty-five and a half seconds to fifteen point two. I want to be careful here. The two configurations produce different output formats, so this should be read as a property of the pipeline, not as an isolated effect of ontology access.

## Slide 14
Ontology-Grounded LLM Planning · IEEE RO-MAN 2026
13
RESULTS · PER SCENARIO
The gap widens exactly where the scene changes
Chart: 
| Object moved | Grasp failure | Blocked object | Clear table (nominal)
LLM-only (text) | 20 | 20 | 40 | 40
Ontology-grounded | 60 | 80 | 80 | 100
Nominal clearing
5 / 5 trials completed by the proposed method; the text-only baseline reached 40%.
Blocked object
Support relations tell the planner what must be removed first — 80% vs 40%.
Grasp failure
Reconstructing the state after a failed grasp recovers the task — 80% vs 20%.
Object moved
Hardest case: the planner must reinterpret a scene that changed spatially — 60% vs 20%.
Five trials per scenario, per method (Table IV).
Notes: [ 10:30 - 11:20 ] PER-SCENARIO RESULTS Here is the same comparison per scenario, five trials each. Under nominal conditions the proposed method clears the table in all five trials, against forty percent for the baseline. When an object is blocked, eighty against forty. Support relations tell the planner what has to come off first. Under grasp failure, eighty against twenty. Reconstructing the state lets the system retry, instead of continuing a plan that is already dead. When an object is moved, sixty against twenty. This is the hardest case, because the planner has to reinterpret a scene that changed spatially.

## Slide 15
Ontology-Grounded LLM Planning · IEEE RO-MAN 2026
14
DISCUSSION
What this shows — and what it does not
What the results support
Tight coupling is what matters
Keeping the planner tied to a world model that is updated during execution improves both initial plan consistency and recovery.
Recovery without extra prompting
Replanning is driven by state reconstruction from ontology and simulator, not by telling the LLM that something went wrong.
Limitations we state openly
Feasibility is still only 44%
The framework continues to fail in a considerable number of trials, before or during execution.
Spatial change remains hardest
Object-moved disturbances stay below blocked-object and grasp-failure recovery.
Narrow evaluation scope
One household task family; ambiguous instructions and mid-task correction are not systematically evaluated.
Notes: [ 11:20 - 12:00 ] DISCUSSION AND LIMITATIONS So what do these numbers show, and what do they not. They support two things. The coupling between planning and world state produces the improvement, not the ontology as a static knowledge source. And recovery happens without any extra cue to the model. The limitations are clear. Feasibility is still forty-four percent: better than the baseline, but not solved. Spatially changed scenes remain the hardest case. And we cover a single task family with a fixed instruction.

## Slide 16
CONCLUSION
The reliability of LLM-based task planning depends on how tightly planning is connected to world-state representation and execution feedback.
Plans from a grounded scene
Not from free text: ontology semantics merged with simulator geometry.
Validated before execution
Symbolic checks and bounded repair keep infeasible plans off the robot.
Revised during execution
State reconstruction and replanning turn a failed skill into a recoverable step.
Next →
Richer interaction settings and more diverse household manipulation tasks · a systematic comparison between VLM-based grounding and the symbolic ontology grounding used here.
15
Notes: [ 12:00 - 12:35 ] CONCLUSION To summarise. We plan from a grounded representation rather than from text, we validate before execution, and we revise that representation during execution. Against a text-only baseline, this produced more feasible plans, higher task success, and clearly better recovery under disturbances. Next: richer interaction settings, more household tasks, and a comparison between VLM-based grounding and the symbolic grounding used here. Thank you. I am happy to take questions. (Advance to the final slide, then stop talking.)

## Slide 17
Thank you
Questions are welcome.
Ontology-Grounded LLM Planning for Robust Table-Clearing Robot Manipulation
Satuk Buğrahan ÖZTÜRK · Ahmet COŞKUNÇAY · Erhan ÖZTOP · Barış ÖZYER
Supported by the Atatürk University Scientific Research Projects Coordination Unit (BAP), reference number FDK-2024-14650.
Notes: Q&A BACKUP. Every answer is written out. Read it, then stop - do not keep adding. Q: Why such a small model, Qwen two point five with three billion parameters? A: It runs locally and keeps the loop fast, and it makes the effect of grounding easier to measure. The pipeline is model-agnostic, and a stronger backend would most likely lift both configurations. Q: Isn't the baseline too weak? Eight percent feasibility seems very low. A: Both configurations use the same validator, the same skills and the same replanning mechanism. The baseline is weak precisely because a textual summary gives the planner no reliable way to respect support relations or the holding state. Q: Why is feasibility still only forty-four percent? A: Most of the remaining failures come from grasp verification, and from scenes whose spatial context changed after planning. That is exactly the case we flag as remaining work. Q: Doesn't the ontology simply encode the answer? A: The ontology encodes types, poses, support relations, and default storage targets. The ordering of the actions, the feasibility reasoning, and the recovery are still produced by the planner. Q: How does this scale beyond table clearing? A: The ontology was defined manually for this domain, so extending it requires new classes, relations, targets and constraints. For a larger ontology we would need task-conditioned queries, so that only the relevant knowledge enters the prompt. Q: Why is the proposed method faster? A: Because the two configurations produce different output formats. That is why we report the gain at the pipeline level, and not as an isolated effect of ontology access. Q: Have you run this on a real robot? A: Not yet. The evaluation is in simulation, in PyBullet. The skill interface is designed so that the symbolic layer stays unchanged when the skills are replaced. Q: How were the disturbances injected? A: After the initial plan had already been generated, during execution. Differences between the ontology and the simulator are recorded, but they do not trigger replanning by themselves. Only a skill-reported failure does. Q: Did you test ambiguous instructions? A: Not systematically. The conditions I reported today use a fixed instruction, and handling ambiguity is future work. If you do not know the answer: "That is a good question, and we have not tested that. I would be happy to discuss it afterwards."